## Slide 1
Speed Control of DC motor using PWM
Created by Group 7
Walchand College of Engineering, Sangli
Course: Microcontroller and Peripheral Interfacing

## Slide 2
Name | PRN
Aditya Pachore | 21410066
Vishvajeet Jagtap | 214110059
Harsh Bandgar | 21410045
Tanuj Joshi | 21410051
Rajwardhan Vichare | 21410058
Presenters:
Guided By: Mr. S.R. Khedkar

## Slide 3
Table of Content
  Introduction
  Objectives
  Components Required
  Circuit Diagram
  Block Diagram
  Algorithm
  Advantages
  Conclusion

## Slide 4
Introduction
Aim of developing thus project is to control the speed of dc motor. Advantage of dc motor is speed-Torque relation can be varied almost of any required form .To achieve the speed control an electronic technique Called Pulse Width Modulation is used which generate high & low pulses .Microcontroller is used to generate a PWM using a timer interrupt and the duty cycle as per requirement .
We are also using L298N motor driver Module which can control up to 4 dc motor 2 with direction control and 2 with speed control.

## Slide 5
Objectives
1. Configure L298n and 8051 microcontroller.
2. Design algorithm to generate PWM for speed control of DC Motor.
3. Design and implement a user interface for speed control of the DC motor.

## Slide 6
Components
  Microcontroller-8051
  DC Motor(12V)
  L298n Motor Driver
  LCD 16*2
  Push buttons

## Slide 7
Proteus Circuit

## Slide 8
Block Diagram

## Slide 9
  Configure the timer0 of 8051 in mode 1 for 16-bit timer operation
  Calculate the timer0 reload value for the desired PWM frequency
  Calculate the duty cycle
  Set the duty cycle of the PWM signal
  Connect the PWM output pin of the 8051 to a driver circuit that can control the motor speed based on the PWM signal
  Initialize the timer0 and start it.
Algorithm

## Slide 10
  In a loop, vary the duty cycle of the PWM signal by changing the value
  Delay for a short period between each change in duty cycle to allow the motor to respond to the new PWM signal
  Repeat above steps until the desired motor speed is achieved
  Make motor 0
Algorithm

## Slide 11
Why PWM?

## Slide 12
Various Technique
A variable resistor or a potentiometer to vary the voltage supplied to the motor, which in turn, controls the speed of the motor.
1)Analog Control
2)Frequency Modulation
The frequency of the voltage supplied to the motor is varied, rather than the duty cycle.

## Slide 13
Various Technique
3)PWM(Pulse Width Modulation)
Their are two ways to generate pulse width modulation signal using microcontroler :
1)Using timers of 8051'
2)Switch a particular pin high and low.

## Slide 14
Advantages of PWM
  Efficiency
  Precise Control
  Low Heat Generation
  Easy to Implement
  Compatibility

## Slide 15
Conclusion

## Slide 16
Future Scope:
i)Remote Control Integration
ii)Closed-Loop Control
iii)Multi-Motor Control

## Slide 17
Thank You